## Background and earlier markings still in use

The Swedish wood packaging programme is built upon the Swedish official approval of sawmills, which was introduced 1997 by the Swedish Board of Agriculture with the aim to make the export inspection of sawn wood more efficient. The sawmill approval is a volunteer system in which the kilns will be thoroughly technically investigated and approved according to the temperature scheme, minimum temperature of 56(C during at least 30 minutes in the core of the wood for all wood sizes in question.

In 1999 some countries required treatment according to the KD 56/30 programme for all wooden products including wood packaging. This caused a growing demand from Swedish export industries for export inspections. Huge amounts of consignments were to be inspected with shipments spread over a longer time period. The most efficient way of export inspection was found to be a production control and the authorization of an official marking. The Swedish wood packaging programme was borne.

By using solely wood from approved sawmill kilns, wood packaging producers also could be authorised to use the same official marking. In this early approval system the wood packaging were marked with the same logo as sawn wood.

The consequence of the early start of the Swedish system and the transitional period without the IPPC logo means that many pieces of approved Swedish wood packaging with older markings are circulating on the market and will be so for some years. The different templates are shown below.

### Old Swedish marking 1

+ Company name

### Older Swedish marking 2

When the international standard ISPM 15 was decided in 2002, the use of the official registration number and DB for debarking was added in the marking.

+ DB SE-yyxxxx

### Older Swedish marking 3

During the transitional period with the withdrawn IPPC-logo some companies were recommended to use the more legible letter combination from the standard but without any logo, where the SE-yyxxxx indicated the official registration number.

HT KD 56(C/30 min DB + SE-yyxxxx